## Slide 1
Optimizing Linux Boot Time
This session gives an overview of methods for optimizing the boot time of a Linux system
July 2012
LAB: http://processors.wiki.ti.com/index.php/Sitara_Linux_Training

## Slide 3: Pre-work Check List
Installed and configured VMWare Player v4 or later
Installed Ubuntu 10.04
Installed the latest Sitara Linux SDK and CCSv5
Within the Sitara Linux SDK, ran the setup.sh (to install required host packages)
Using a Sitara EVM, followed the QSG to connect ethernet, serial cables, SD card and 5V power
Booted the EVM and noticed the Matrix GUI application launcher on the LCD
Pulled the ipaddr of your EVM and ran remote Matrix using a web browser
Brought the USB to Serial cable you confirmed on your setup (preferable)

## Slide 4: Agenda
What is Fast Boot?
Boot Process Overview
Measuring Boot Time
Identifying the Boot Steps
Profiling
  U-boot
  Linux Kernel
Optimization Techniques
  U-boot
  Linux Kernel
  File System

## Slide 5: What is Fast Boot?
Fast boot refers to minimizing the boot time of a system. The boot time of the system is the time it takes from the application of power to the system becoming “available”
“Available” has a lot of different meanings depending on the user expectations.
  Appearance of the home screen for devices like cell phones
  An audible tone or LED indicator
  A Linux prompt
  Becoming discoverable on the network
  Having a key peripheral become available
The above variances show why the Sitara Linux SDK is generally not fully optimized for boot time. Each user can have a different target and a generic SDK cannot satisfy all user targets
  There are also many features that make for a good development environment, but which do not make for a fast booting environment

## Slide 6: Boot Process Overview

## Slide 7: Measuring Boot Time
There are a couple of different options for measuring boot time. You can use a C program that time stamps each line on the serial port.
  http://processors.wiki.ti.com/index.php/Measuring_Boot_Time
  Compile with “gcc tstamp.c -o tstamp”
  This can also be invoked as “cat /dev/<TTY DEVICE> | tstamp
RealTerm for Windows supports time stamping the incoming serial data
  http://realterm.sourceforge.net/
  Support logging in Unix date format
  Ability to log directly to a file
  Ability to stop logging after a predefined time
  No need to switch terminal for interactive session
TeraTerm for Windows can now log time as well but does not give elapsed time measurements.

## Slide 8: Measuring Boot Time - Cont
Using the C program approach you will see output like:
18.066 0.093: Thu Jun 28 11:56:00 UTC 2012
INIT: Entering runlevel: 5
18.262 0.175: Starting system message bus: dbus.
18.280 0.018: Starting Hardware abstraction layer hald
19.474 1.194: Starting Dropbear SSH server: dropbear.
19.499 0.025: Starting telnet daemon.
19.538 0.039: Starting network benchmark server: netserver.
19.569 0.031: Starting syslogd/klogd: done
19.629 0.060: Starting thttpd.
19.731 0.102: Starting PVR
20.158 0.427: Starting Lighttpd Web Server: lighttpd.
20.176 0.018: 2012-06-28 11:56:02: (log.c.166) server started
In the above output you can see that starting the Dropbear SSH server takes 1.194 seconds.
  If you do not need SSH you can save 1.194 seconds by disabling Dropbear
  Disabling Dropbear is as simple as removing the S10dropbear init script from the /etc/rc5.d directory

## Slide 9: Identifying the Boot Steps
One of the first things to help in optimizing boot time is to be able to recognize the markers indicating where a new part of the boot process starts
SPL
  The first newline character received on the serial console marks the start of SPL
U-boot
  The banner containing the U-boot version indicates the start of u-boot
  U-Boot 2011.09 (Jun 28 2012 - 11:20:36)
Linux Kernel
  First line after the below line indicates the start of the Linux kernel
  Uncompressing Linux… done, booting the kernel
File System
  The below line indicates the transition to the file system Init process
  INIT: version 2.86 booting

## Slide 10: Profiling the Boot Loaders
There is no direct profiling support in the boot loaders, but the serial print times can still be very useful
For example, when booting the kernel image you will see output like:
5.335 0.010: ## Booting kernel from Legacy Image at 80007fc0 ...
5.339 0.004: Image Name: Arago/3.2.0-psp04.06.00.08.sdk/a
5.344 0.005: Image Type: ARM Linux Kernel Image (uncompressed)
5.348 0.004: Data Size: 3164688 Bytes = 3 MiB
5.350 0.002: Load Address: 80008000
5.352 0.002: Entry Point: 80008000
6.273 0.921: Verifying Checksum ... OK
6.276 0.003: XIP Kernel Image ... OK
6.310 0.034: OK
Notice that almost a second is spent verifying the kernel image checksum.
If your system doesn’t do anything about a bad image, why spend time verifying it?
  This verification can be disabled by setting the “verify” u-boot parameter to n at the u-boot command prompt
  u-boot# setenv verify n

## Slide 11: Profiling the Linux Kernel
One of the simplest ways to profile the Linux kernel is to configure “CONFIG_PRINTK_TIME” for the Linux kernel. On most recent kernels this is enabled by default.
  This adds the time since the kernel was booted in [ ]’s before each line
[ 2.029785] mmc1: card claims to support voltages below the defined range. T.
[ 2.048583] mmc1: queuing unknown CIS tuple 0x91 (3 bytes)
[ 2.055053] mmc1: new SDIO card at address 0001
[ 3.986724] PHY: 0:00 - Link is Up - 100/Full
[ 4.015808] Sending DHCP requests ., OK
[ 4.036254] IP-Config: Got DHCP answer from 0.0.0.0, my address is 128.247.10
[ 4.044586] IP-Config: Complete:
[ 4.047973] device=eth0, addr=128.247.105.20, mask=255.255.254.0, gw=12,
[ 4.056182] host=128.247.105.20, domain=am.dhcp.ti.com, nis-domain=(non,
[ 4.063781] bootserver=0.0.0.0, rootserver=0.0.0.0, rootpath=
  In The above output we can see that it takes almost 2 seconds to get the network Phy Link up and obtain a DHCP IP address.
    Depending on network speed this could be longer. In the case where there is no DHCP server this can take minutes to timeout.
    Setting “ip=off” in the bootargs will bypass kernel network configuration while still allowing you to configure the network in user space.
      setenv ip_method off

## Slide 12: Profiling the Linux Kernel - Cont
Instrument kernel initialization. This will help you find which static drivers in the kernel are taking the most time to initialize
  Add “initcall_debug” to the bootargs in u-boot. With recent u-boots this can usually be done using:
  setenv optargs initcall_debug
  saveenv
  When the Linux system is booted you can view these initcall lines using “dmesg | grep initcall”
  [ xxxxx] initcall <init function> [<module>] returned 0 after <time> usecs
  These lines can be sorted using the commands below to help find the modules with the largest init times
    If CONFIG_PRINTK_TIME is enabled
      dmesg | grep initcall | sort -k8 -n
    If CONFIG_PRINTK_TIME is not enabled
      dmesg | grep initcall | sort -k6 -n
  It is possible to graphically view these initcall times using the bootgraph script in the Linux kernel sources. This requires CONFIG_PRINTK_TIME to be enabled
    cat <bootlog> | perl <kernel source dir>/scripts/bootgraph.pl > boot.svg
Additionaly you can use other tools to help you analyze the Linux kernel such as:
  Linux Trace Toolkit (LTTng)
    Timing for certain kernel and process events
  Oprofile
    System wide profiler
  Bootchart
    Visualizes boot process

## Slide 13: Areas of Optimization
Optimizations generally fall into two areas
Size
  Reduce the size of binaries
  Remove features not required to reduce component size
Speed
  Optimize for target processor
    Neon optimizations
  Use faster boot media
    NOR/NAND vs. MMC/USB
  Reduce the number tasks leading to boot
    Do not check MMC if booting from NAND
    Do not initialize network if booting from MMC
  Reduce initialization operations
    Do not bring up network during boot if not required
    Do not start an SSH server on a device with no network

## Slide 14: U-boot Optimization Techniques
Reduce environment size so that less data is read into memory
  CONFIG_ENV_SIZE
Remove Unnecessary Console Print Statements
  In board config file add
    #define CONFIG_SILENT_CONSOLE 1
  In u-boot environment do
    setenv silent 1
Set “bootdelay” to 0
Disable un-used peripherals such as USB/MMC/Ethernet/UART
Modify the config file for your device in <u-boot sources>/include/configs. i.e am335x_evm.h
  Avoid long help text for the u-boot commands to save space
    #undef CONFIG_SYS_LONGHELP
  Use simple parser - instead of hush
    #undef CONFIG_SYS_HUSH_PARSER
  If no USB/NAND/MMC/SPI/NOR(FLASH)
    #undef CONFIG_USB_*
    #undef CONFIG_NAND
    #undef CONFIG_MMC
    #undef CONFIG_SPI
    #undef CONFIG_FLASH_*

## Slide 15: U-boot Optimization Techniques - Cont
Remove -g option from the compiler
Other Ideas
  Disable UART boot
  Remove Image Verification (covered before)
  Perhaps try uncompressed image
  Verify that kernel image is read to the proper memory location

## Slide 16: Linux Optimization Techniques
Remove un-necessary drivers/features from kernel configuration
  Reduces driver initialization time
  Reduces kernel size
Build non-fast boot drivers as modules
  Load them after the system is booted when there is more time
Disable console output using “quiet”
  Displaying messages on console takes time
  Setting the “quiet” option in the bootargs disables display on console but messages are still logged
    u-boot# setenv optargs quiet
  Remove un-used consoles. These take time to initialize.
    These can be removed in the /etc/inittab file on the target file system
  It is possible to completely disable printk but this will eliminate a lot of debug information

## Slide 17: Linux Optimization Techniques - Cont
Defer module init calls
  It is possibly to defer module init calls without having to build the modules dynamically.
  This requires modifying the kernel
  For modules that are not needed at boot replace the “module_init()” function calls to “deferred_module_init()”
  Once the system booted the deferred calls can be executed by doing:
    echo 1 > /proc/deferred_initcalls
  Additional details at http://elinux.org/Deferred_Initcalls
Remove the -g option from the compile
Disable kernel debugging features
  Kernel debugging
  Debug Filesystem (NOTE: Some features may need this)
  Tracers
Remove any instrumentation you may have added such as initcall instrumentation.

## Slide 18: Linux Optimization Techniques - Cont
Pre-set loops per jiffy
  You just need to measure this once
  Find lpj value in kernel boot messages
    Calibrating delay loop… 718.02 BogoMIPS (lpj=3590144)
  Add the “lpj=3590144” to the bootargs
Use Static IP addressing where possible
  If you don’t need networking then disable it altogether
  If you want networking capability but not NFS then be sure to set “ip=off” on the kernel command line.
Set memory limit with “mem=“ option
  Use only as much memory as needed to avoid DDR initialization time

## Slide 19: File System Optimization Techniques
Use minimal BusyBox file system
  Reduces forking in shell
  Build static of possible to reduce the need for un-used code in the file system
    Be careful because static linking can also cause your file system size to increase dramatically.
Avoid using ramdisk or initramfs
  Must load entire ramdisk from flash into DDR
  May only need a small part at boot time
  i.e. may not need all of glibc but entire library will be loaded into DDR using ramdisk or initramfs
  Buffer cache can keep frequently used files in memory

## Slide 20: File System Optimization Techniques - Cont
Pre-linking
  Avoid run time linking penalty
  Drawback: If library changes app must be rebuilt.
Use tmpfs file system
  No need to initialize file system for non-persistent data
Use split file systems
  Have multiple file system partitions
  Put only the files needed for boot in the root file system partition
  Put other files in second file system which can be mounted after boot

## Slide 21: File System Optimization Techniques - Cont
Strip executables
  Removes un-needed symbols and reduces size
Avoid udev for static systems
  If the system doesn’t change then make device nodes manually rather than udev creating them
  Hotplug-daemon can still run later to add additional devices that are plugged in
Disable init scripts that start unneeded services
Use GNU_HASH to make dynamic linking faster (This is the default for the SDK)
Use systemd for parallel initialization

## Slide 22: Credits/Sources
http://processors.wiki.ti.com/index.php/Optimize_Linux_Boot_Time
  by Sanjeev Premi
http://elinux.org/Boot_Time